ASSESSMENT OF UNCERTAINTIES RELATED TO SEISMIC HAZARD USING FUZZY ANALYSIS

N. Jorjiashvili*, T. Yokoi**, Z. Javakhishvili*

Abstract

Seismic hazard analysis in the last few decades has become a very important issue. Recently, new technologies and available data have been improved that have helped many scientists to understand where and why earthquakes happen, the physics of earthquakes, etc. Scientists have begun to understand the role of uncertainty in seismic hazard analysis. However, how to handle existing uncertainty is still a significant problem. The same lack of information causes difficulties in quantifying uncertainty accurately.

Usually attenuation curves are obtained in a statistical manner: regression analysis. Statistical and probabilistic analysis show overlapping results for the site coefficients. This overlapping takes place not only at the border between two neighboring classes, but also among more than three classes. Although the analysis starts from classifying sites using geological terms, these site coefficients are not classified at all. In the present study, this problem is solved using fuzzy set theory. Using membership functions, the ambiguities at the border between neighboring classes can be avoided. Fuzzy set theory is performed for southern California in the conventional way. In this study, standard deviations that show variations between each site class obtained by fuzzy set theory and the classical manner are compared. Results of this analysis show that when we have insufficient data for hazard assessment, site classification based on fuzzy set theory shows values of standard deviations less than those obtained use the classical way, which is direct proof of less uncertainty.

Keywords: Seismic Hazard, Uncertainty, Fuzzy Analysis, Attenuation Relation.

Introduction

An estimation of expected ground motion is fundamental for earthquake hazard assessment. Generally, ground motion and damage are influenced by the magnitude of the earthquake, the distance from the seismic source to the site, the local ground conditions and the characteristics of buildings (Atkinson, 2004). Empirical attenuation relation, a practical way to estimate ground motion parameters, gives information about how these parameters depend on the above mentioned source, path and site effects (Field, 2000). This, namely ground condition, must be considered, because the same earthquake recorded at the same distance may cause different damage according to ground conditions (Irikura et al. 2004).

In conventional approaches, grouping or classification is done for strong motion observation sites based on a priori given information expressed by geological terms (Wills, 2000). Then, regression analyses are applied to the ground motion parameters (peak ground acceleration (PGA), response spectra (SA), etc.) observed at each of these classes (Field 2000). Although amplification factors are assigned to all stations used in analyses, the majority of the sites in that seismic hazard are assessed; but, any ground motion recorded which is no available, does not have this assigned value. Therefore, the mean value of each class has to be used for them in order to make a seismic hazard assessment.

The usage of the mean value, however, brings an uncertainty for site amplification into the obtained seismic hazard. Its cause is a widely scattered amplification factor, even in the same site class. Molas and Yamazaki (Molas and Yamazaki 1995), e.g., show the list of site factors for PGA. Significant overlap of widely scattered distribution is observed among different classes. It can be interpreted that the classification in geological terms done prior to the regression analysis may be incorrect, i.e., the data scattered far from the mean value should be reclassified into another, because the borders between classes are essentially ambiguous, e.g., due to weathering etc. This can also cause one to misjudge the site classification when attenuation relation is applied to sites that do not have any ground motion record. The reliability of judging varies site to site, depending on the available information, i.e., fresh cut along a road in a site and ground covered by newly filled sand in another site. It is possible to imagine that there exists a level of uncertainty, depending on available information at each site.

In the present study, fuzzy set theory is applied in order to handle the uncertainty caused by the site classification based on geological terms and its level of uncertainty.

METHOD OF ANALYSIS: FUZZY SET THEORY

Basics of Fuzzy Set Theory

# Fuzzy set theory is an extension of conventional (crisp) set theory. It handles the concept of partial truth (truth values between 1 (completely true) and 0 (completely false)). It was introduced by Prof. Lotfi A. Zadeh of UC Berkeley in 1965 as a means to model vagueness and ambiguity in complex systems (Zadeh 1965).

The Membership Function

For the universal  and given the membership-degree function  the fuzzy set  is defined as  . The membership function  quantifies the grade of membership of the elements x to the fundamental set. The value 0 means that the member is not included in the given set; 1 describes a fully included member. The values between 0 and 1 characterize fuzzy members (De Campos and 1989).

Some operations and arithmetic on fuzzy sets and numbers

Let  and be two fuzzy subsets of universal set  and  and  corresponding degree of membership of x in  and  respectively. Then following operations on sets can be defined    (Schmucker 1984).

Intersection:  ,                                     (1)

Union:  .                                    (2)

The support of a fuzzy set  is the ordinary subset of (Dubois and Prade, 1988):

,                                                        (3)

When we want to exhibit an element  that typically belongs to a fuzzy set , we may demand its membership value to be a greater than some threshold. The ordinary set of such elements is the -cut  of ,

,                                                            (4)

The membership function of a fuzzy set  can be expressed in terms of the characteristic functions of its -cuts according to the formula (Dubois et al. 1988):

,                                                       (6)

where means the supremum, i.e. the least upper bound.

(7)

A fuzzy subset  of a classical set  is called normal if there exists  such that. Otherwise  is subnormal. An -level set of a fuzzy set  of  is a non-fuzzy set denoted by  and is defined by

(8)

where  denotes the closure of the support of  (the smallest set which is closed with respect to some operations in set theory as it is known in classical set theory). A fuzzy set  of  is called convex if  is a convex subset of ,  (Carlsson and Fullér 2000).

A fuzzy number A is a convex, normalized fuzzy set whose membership function is at least segmentally continuous and has the functional value  at precisely one element.

For the fuzzy number  the interval of confidence for the level of presumption ,  can be defined as follows:

,                                                       (9)

Let   and be two fuzzy numbers and  and  their intervals of confidence for the level of presumption ,. Then the addition can be defined as follows:

,                           (10)

and subtraction can be written as follows:

.                           (11)

Suppose we have  fuzzy numbers as  then

,                                                               (12)

for the interval of confidence at the level  of  . Then, defining the mean as

,                                                                        (13)

,                                                                        (14)

the mean interval of confidence at the level of  of the mean fuzzy number  is described as

.                                                                          (15)

(15) and is called the fuzzy expected average (Kaufmann et al. 1985).

If  and  are a sequence of fuzzy sets, then the fuzzy weighted average of the ’s using  ’s as weights, is defined as follows:

.                                                                           (16)

The fuzzy arithmetic operations, summation, multiplication and division, which are used in equation (16) are defined as follows (Schmucker 1984):

If

,                                                                     (17)

,                                                                      (18)

where  and  are integers;  and  are membership functions that characterize the fuzzy sets  and , respectively, then the fuzzy addition is defined as follows:

,                                     (19)

The fuzzy summation is a repeated process of the fuzzy addition.

The fuzzy multiplication is defined as follows:

,                                      (20)

and the fuzzy division is defined as:

.                                       (21)

Ranking method

The ranking method implemented in this study is based on a scoring function that measures a TFN’s (trapezoidal fuzzy number) center of gravity (centroid) along the -axis (Fig 1).

For fuzzy numbers with a non-zero area, the score is calculated as follows:

,                              (22)

where  is the core and   and  are the left and right bandwidth respectively.

Fig 1 trapezoidal fuzzy number (TFN) and its centroid.

Expected value and Standard Deviation for trapezoidal fuzzy number

Let  be a fuzzy number with . The possibilistic (crisp) mean (or expected) value of is defined as follows (23):

,                                        (23)

i.e.  is nothing but the level-weighted average of the arithmetic means of all -level sets.

The variance (possibilistic) of  is defined as follows (24):

(24)

i.e. the possibilistic variance of  is defined as the expected value of the squared deviations between the arithmetic mean and the endpoints of its level sets.

In case of  trapezoidal fuzzy number

(25)

and

.                                           (26)

where  corresponds to -level in equation (23) and (24). Standard deviation is obtained as follows:

.                                                                           (27)

Uncertainty Scaling for Reliability of Classification

In the linguistic approach to decision analysis, the use of linguistic labels implies a level of uncertainty.  The quantitative uncertainty is created by uncertainty in measurement or estimation of the source variable on which the label is placed, which also directly impacts the decision process (Debruin and Bregt 2001). In the case of environmental value for example, the estimate provided is usually based on incomplete information, due to our limited understanding of the complex nature of natural systems (Christensen 1996). The question arises: how to include quantitative uncertainty into the analysis process? The operation can be described as follows:

,                                      (28)

where ,   are shown in Fig 1. Schematically, uncertainty scaling operation is shown in Fig 2.

Fig 2 Graphical representation of uncertainty scaling.

is the uncertainty scaling operation;  is the uncertainty term used in the scaling operation;  is the base uncertainty term (the term which represents the inherent quantitative uncertainty in the -scaled term). In this study we chose ,

.                                                                         (29)

Data used in the present study

Data used here were downloaded via the Internet from the COSMOS VIRTUAL DATA CENTER (http://db.cosmos-eq.org/scripts/adv_search.plx, hereafter written CVDC) for California (latitude range between 32N and 36N), for 281 stations in southern California and 28 earthquakes with magnitudes larger than 5.0 determined between 32N and 36N. In this database, the 1994 Northridge earthquake is also included (M=6.7) (Steidl and Lee 2000). There, stations are classified by their surface geology as summarized in Table 2. In the present study, BC class (Wills et al. 2000) is recognized in the possible range (left bandwidth) of B class here. At the same time it is recognized in the possible range (right bandwidth) of C class. The same treatment is done for CD and DE classes.

Table 1: Summary of the data used ,downloaded from COSMOS VIRTUAL DATA CENTER (http://db.cosmos-eq.org/scripts/adv_search.plx) with the parameters metioned above. The legend of site classes with geological terms (Wills et al. 2000).

| Site Class CVDC | Number of stations | Number of stations with Vs | Mean Value (m/sec) | Standard Deviation (m/sec) |
| --- | --- | --- | --- | --- |
| A | 8 | 8 | 1857.6 | 256 |
| B | 17 | 17 | 871.4 | 238 |
| BC | 47 | 47 | 728 | 209.2 |
| C | 132 | 132 | 470.8 | 139 |
| CD | 180 | 180 | 368 | 96 |
| D | 120 | 120 | 286 | 68 |
| DE | 45 | 45 | 226 | 36 |
| E | 4 | 4 | 157 | 45 |

Table 2: Site classes are used here in relation with others. The mean values and the standard deviations are calculated newly for the site classes of the present study.

| Present Study | (Wills et al. 2000) | (m/sec) NEHRP | (m/sec) used by Field (2000) |
| --- | --- | --- | --- |
| Site Class | Mean Value (m/sec) | Standard Deviation (m/sec) | Site Class | Vs(m/sec) |  |  |
|  |  |  |  | Expected Value | Mean Value | Standard Deviation |  |  |
| A | 1857.6 | 256 | A | N/A | N/A | N/A | 1500< | N/A |
| B | 1066 | 391 | B | 760< | 686 | 275 | 760<<1500 | 1000 |
|  |  |  | BC | 555<<1000 | 724 | 368 | N/A | 760 |
| C | 471 | 219 | C | 360<<760 | 464 | 147 | 360<<760 | 560 |
|  |  |  | CD | 270<<555 | 372 | 98 | N/A | 360 |
| D | 285 | 76 | D | 180<<360 | 301 | 104 | 180<<360 | 270 |
|  |  |  | DE | 90<<270 | 298 | 225 | N/A | 180 |
| E | 157 | 45 | E | Vs<180 | 163 | 31 | <180 | N/A |

Field (Field 2000) obtained attenuation relations for PGA and SA at the period equal to 0.3, 1.0 and 3.0 sec as follows.

,      (30)

where  is the predicted natural logarithm of the ground motion parameter (e.g., ),  the moment magnitude,  the closest distance to the vertical projection of rupture (in km), and  the average 30-meter shear-wave velocity at the site (m/sec), the values of which are listed in Table 2 .  is an arbitrary reference site velocity; here it’s taken as 760m/sec in all cases, and  a fictitious depth needed to prevent zero distance.  The other parameters ( and ) are solved by regression analysis from empirical data (Field 2000).

Aplication of fuzzy set theory

Designing of membership function

In the present study, non-symmetrical linear trapezoidal membership functions are used for simplicity in order to capture the vagueness in geological classification. A standard linear trapezoidal fuzzy number (TFN) can be represented completely by a quadruplet  as shown in Fig 1. It is also useful that crisp numbers  can be represented in trapezoidal form (Bailey 2003).

In the CVDC database, average shear-wave velocity to 30m () is assigned to site classes as an indicator of site response (Table 1). The legend in geological terms of the site classes is found in the paper of Wills et al. (Wills et al. 2000). Then,  is selected as the variable parameter for membership functions.

First, the distribution function against  is made for each site class of the present study and the mean values  and the standard deviations  in statistical (classical) meaning, andthe distribution function normalized by its value at  is calculated.

Then, the membership function  is given as follows.

,                                       (31)

where denotes shear wave velocity values on the left side of the mean value, denotes shear wave velocity values on the right side of the mean value,   means the minimum value of shear wave velocity obtained in the certain site class,  the maximum value for the same site class. From (31) which the uncertainty range can be determined (, ).

(32)

where  and denote the values of  at the left and right sides of , both of them that give 0.1 for the normalized distribution function. The data of which  is located between  and are recognized “true”, whereas those outside of the range limited by andare “false”. Those in the ranges between  and , and between and  are “partially truth-partially false”. After the linear trend line is added on the left side from the   and on the right side from the  in order to obtain trapezoidal membership function.

Fig 3: Schematic figure for the process to obtain membership function based on the normalized distribution function.

Giovinazzi and Lagomarsino (Giovinazzi and Lagomarsino 2004) express the four corners of TFN using , , ,  that correspond , , , in Fig 1, respectively. andare called the lower and the upper bounds of the possible range.  and are called the lower and the upper bounds of the uncertainty range. The most probable value is obtained as the mean value of the trapezoidal membership function as shown in equation (25). Table 3 shows these five parameters for the five classes used in the present study.

Table 3: Parameters of TFN for five site classes

| Site Class |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| A | 1100 | 2000 | 2025 | 2050 | 2100 |
| B | 480 | 770 | 935 | 1100 | 1500 |
| C | 350 | 370 | 425 | 480 | 770 |
| D | 175 | 270 | 310 | 350 | 370 |
| E | 100 | 160 | 167.5 | 175 | 270 |

The obtained membership function for each site class looks as shown in Fig 4.

First, for site class indexes again centroids of trapezoidal membership functions are used shown in equation (22).

Fig 3: Site classification considering shear-wave velocity values.

Table 3: Site class index and standard deviation for all site classes for classical and                                                         fuzzy case for T=1.0sec.

| Site Class | values | classical | by centroid of trapezoidal function |
| --- | --- | --- | --- |
| A Class | Site class index (m/sec) | 1857.6 | 1799.8 |
|  | stand.deviat. (m/sec) | 256 | 214.8 |
| B Class | Site class index (m/sec) | 1066 | 966.5 |
|  | stand.deviat. (m/sec) | 391 | 291 |
| C Class | Site class index (m/sec) | 471 | 490.1 |
|  | stand.deviat. (m/sec) | 219 | 132.7 |
| D Class | Site class index (m/sec) | 285 | 273.4 |
|  | stand.deviat. (m/sec) | 76 | 53 |
| E Class | Site class index (m/sec) | 157 | 159.9 |
|  | stand.deviat. (m/sec) | 45 | 36 |

Uncertainty Scaling

Once we obtain trapezoidal membership function for each site class, then we can use the uncertainty scaling operation for reliability of classification. Using such scaling operation we can obtain different membership functions which correspond to each level of uncertainty as shown in Fig 4. Then station coefficients can be obtained by several ways, depend on our purpose, which are shown later based on some examples.

Our purpose is to handle uncertainty. For this purpose we use the uncertainty scaling. We choose a different level of uncertainty, such as ‘very uncertain’, ‘uncertain’, ‘moderately certain’, ‘certain’ and ‘very certain’, and give them some weights due to treatment of uncertainty. Then we can choose a specific level of uncertainty and perform fuzzy analysis for this level; or, we can consider some levels of uncertainty, neglect others, or otherwise leave only a certain level. We have many options depending on our purpose.

Then fuzzy analyses were applied for second type classification.

Fig 4 Uncertainty Scaling.

Then we define uncertainty semantically, as shown in Fig 4. Then we use scaling operation shown in equations (28) and (29). In those equations instead of , values of the membership function are used as an argument of  function. For example, for B site class we can get uncertainty scaling as follows:

For ‘very certain’ case (weight: =0.1)

,                                                 (33)

and as an interval:

,                               (34)

For ‘certain’ case (weight: =0.3)

,                                               (35)

and as an interval:

,                             (36)

For ‘moderately certain’ case (weight: =0.5)

,                                               (37)

and as an interval:

,                                  (38)

For ‘uncertain’ case (weight: =0.7)

,                                             (39)

and as an interval:

,                              (40)

and for ‘very uncertain’ case (weight: =0.9)

,                                               (41)

and as an interval:

,                             (42)

where  is a level of confidence and

.

Fig 5 shows uncertainty scaling for B site class. The blue line shows the membership function obtained by the second type of fuzzy classification. Again, as with other cases, ‘moderately certain’ corresponds to this classification itself.

Fig 5 Uncertainty Scaling for B site class.

Site class indexes for the other two cases are performed two different ways. One of them is a combined approach, considering only from ‘very certain’ up to ‘moderately certain’ levels of uncertainty. Fuzzy intervals of each level of confidence from 0 up to 1 are also used here. Then expected and maximum values are calculated (Table 4). We use both of these values for the calculation of the site class index (Kaufmann 1988).

Table 4 Expected values for each term and all site classes for SA for California

|  | Site Classes | membership | very certain | Certain | mod. certain |
| --- | --- | --- | --- | --- | --- |
| Expected Values | A Cass | 1799.8 | 1695.8 | 1721 | 1799 |
|  | B Class | 966.9 | 960.4 | 963.9 | 966.9 |
|  | C Class | 490.1 | 493.8 | 492 | 489.7 |
|  | D Class | 273.4 | 265.8 | 269.6 | 272.8 |
|  | E Class | 159.9 | 165.1 | 163.4 | 161 |

Table 5 shows site class indexes and standard deviations obtained for B site class for all classical and fuzzy cases for period 1.0 sec. These standard deviations are related to the variation of the station coefficients in site class () for classical and fuzzy cases for B site class and for fuzzy cases obtained using equations (26), (27).

Table 5 Site class indexes and standard deviations for all site classes for classical and  all fuzzy cases                for T=1.0sec.

|  | classical | second type fuzzy classification |
| --- | --- | --- |
|  |  | by centroid of trapezoidal function | combined | very certain | mertain | moderately certain | uncertain | very uncertain |
| A class | Site class index (m/sec) | 1857.6 | 1799.8 | 1798 | 1695.8 | 1721 | 1799 | 1802 | 1813.5 |
|  | Stand.deviat. (m/sec) | 256 | 214.8 | 216 | 168 | 189 | 213 | 228 | 258 |
| B class | Site class index (m/sec) | 1066 | 966.5 | 966.8 | 963.7 | 965.4 | 966.9 | 967.9 | 968.7 |
|  | Stand.deviat. (m/sec) | 391 | 291 | 293 | 188.7 | 239 | 291 | 345 | 399 |
| C class | Site class index (m/sec) | 471 | 490.1 | 491 | 493.8 | 492 | 489.7 | 486.6 | 482.2 |
|  | Stand.deviat. (m/sec) | 219 | 132.7 | 134 | 109 | 121 | 132 | 165 | 218 |
| D class | Site class index (m/sec) | 285 | 273.4 | 274.3 | 265.8 | 269.6 | 272.8 | 276.7 | 283.5 |
|  | Stand.deviat. (m/sec) | 76 | 53 | 53.5 | 43 | 48 | 54 | 65 | 77 |
| E class | Site class index (m/sec) | 157 | 159.9 | 160.2 | 165.1 | 163.4 | 161 | 158.3 | 156.7 |
|  | Stand.deviat. (m/sec) | 45 | 36 | 35 | 29 | 33 | 35.5 | 38 | 46 |

RESULTS of Analysis

Data from the paper (Field 2000) is used as an example for SA. The fuzzy analysis gives smaller values of the standard deviations than those of the classical case for SA.

First, the membership functions for SA are designed by considering existing information about shear wave velocity values. Field (Field 2000) provides the information about site characteristics, i.e., shear wave velocity at the surface. If there is no measurement or any existing information then membership function can be obtained as a linguistic term using a symmetric (quadruplet) membership function but if there is a possibility to obtain some information, then, such information can be used for the design of the membership function as it is done in the present work. Thus, membership functions are obtained more precisely; the site class indexes and the standard deviations are calculated quantitatively. In the fuzzy case, standard deviations are significantly reduced as compared to the classical case (Table 3).

As shown above, the membership functions for SA are obtained in an appropriate manner. Thus, the uncertainty scaling is applied to SA.

DISCUSSION AND CONCLUSION

There are many causes of uncertainty throughout the seismic hazard analysis process. The attenuation relation of ground motion that plays a main role brings many uncertainties into the analysis. The present study focused on the uncertainty related with the site classification for the acceleration response spectra (SA).

In this study, standard deviations that show variations between each site class obtained by fuzzy set theory and the classical means are compared. Results on this analysis show that even when we have very insufficient data for hazard assessment, site classification based on fuzzy set theory shows values of standard deviations less than those obtained in the classical manner, which is direct proof of less uncertainty. The 	example performed in this work shows that variances based on station coefficients significantly reduce in the fuzzy case in comparison with the classical case. As shown here, designing membership function is very important. If we design appropriate membership function we can reduce uncertainty.

Given membership functions allow the application of various methods of fuzzy set theory. In the present study, the uncertainty scaling is selected among them. This method can handle the difference of uncertainty level or reliability of judgment for site classification. For example, if we have to classify site conditions only based on geological information or some other non-numerical information, we use membership function for the ‘very uncertain’ level. If we have some geotechnical measurement or some more precise information, we can select a lower uncertainty level (toward ‘very certain’). Also, not only the standard deviations, but also the site class indexes, can be changed by the uncertainty scaling. This shows a new aspect of the empirical attenuation relation.

All the discussions mentioned above prove the advantage and usefulness of fuzzy set theory, not only for attenuation relation of ground motion, but also in many cases where some primary data are insufficient or ambiguous. Especially for seismic hazard assessment, it is necessary to handle uncertainty, and, fuzzy set theory allows for this. Fuzzy set theory may be useful not only for seismic hazard, but also for all kinds of natural hazards; however, there are many terms which are not understood very well quantitatively which should be considered in hazard assessment.

References

Abrahamson NA, Youngs RR (1992) A stable algorithm for regression analysis the random effect model. Bull. Seism. Soc. Am. Vol. 82,  pp.469-487.

Atkinson GM (2004)  An Overview of Developments in Seismic hazard analysis.  13th World Conference on Earthquake Engineering. Vancouver, B.C., Canada, August 1-6, Paper No.5001.

Bailey D (2003) A decision support system for site selection of large-scale infrastructure facilities using natural language. Proc. Of the conf: Operations research into the 21st cent., pp.1-17. The Austrian Society for Operations Research (AOSM).

Carlsson Ch, Fullér R (2000) Real option evaluation in fuzzy environment. Proc. Of the International Symposium of Hungarian Researchers on Computational Intelligence, Budapest, [ISBN 963 00 4897 3], 69-77.

Christensen NL, Bartuska AM, Brown JH, Carpenter S, D’Antonio C, Francis R, Franklin JF, MacMahon JA, Noss RF, Parsons DJ, Peterson CH, Turner MG and Woodmansee RG (1996) The Report of the Ecological Society of America Committee on the Scientific Basis for Ecosystem Management. Ecological Applications, 6(3): 665-691.

De Campos LM,  MJ (1989) Representation of fuzzy measures through probabilities.  Fuzzy Sets and Systems, Vol. 31, pp. 23-36.

Debruin S, Bregt A (2001) Assessing fitness for use: the expected value of spatial data sets, Int. J. Geographical Information Systems, 15(5): 457-471.

Dubois D, Prade H (1988) Theory  of possibility an approach to computerized processing of uncertainty. Plenm Press, N.Y.

Field EH (2000) Modified Ground-Motion Attenuation Relationship for Southern California that Accounts for Detailed Site Classification and a Basin-Depth Effect. BSSA, 90, 6B, pp. S209-S221.

Giovinazzi S, Lagomarsino S (2004) A Macroseismic Method for the Vulnerability Assessment of Buildings. 13th World Conference on Earthquake Engineering. Vancouver,B.C., Canada, Paper No.896.

Irikura K, Miyake H, Iwata T, Kamae K, Kawabe H, (2004) Recipe for Predicting Strong Ground Motions from Future Large Earthquakes. and Luis Angel DALGUER. 13th World Conference on Earthquake Engineering.  Vancouver,B.C., Canada, Paper No.1371.

Joyner WB, Boore DM (1993) Peak horizontal acceleration and velocity from strong-motion records including records from the 1979 Imperial Valley, California, earthquake, Bull. Seism. Soc. Am. Vol.71, pp.2011-2038.

Joyner WB, Boore DM (1993) Methods for regression analysis of strong-ground motion data, Bull. Seism. Soc. Am. Vol. 83,pp. 469-487.

Kaufmann A (1988) Theory of expertons and fuzzy logic, FSS 28 , N3 pp 295-305.

Kaufmann A, Gupta MM (1985) Introduction to Fuzzy arithmetic, Van Nostrand Reinhold Company Inc. NY

Kramer SL (1996) Geotechnical Earthquake Engineering. Upper Saddle River, New Jersey 07458.

Molas GL, Yamazaki F (1995) Attenuation of Earthquake Ground Motion in Japan Including Deep Focus Events. Bull. Seism. Soc. Am. Vol. 85, N.5, pp.1343-1358.

Schmucker Kurt J (1984) Fuzzy sets, natural language computations, and risk analysis, Computer Science Press.

Somerville P (2000) Seismic Hazard Evaluation. 12th World Conference on Earthquake Engineering. Vancouver, B.C., Canada, Paper No.2833.

Steidl H, Lee Y (2000) The SCEC Phase III Strong-Motion Database, BSSA, 90, 6B, pp. S113-S135.

Steimen S (1973) Uncertainties in Earthquake Scenarios. Dissertation Thesis. Born.

Wills C J, Petersen M, Bryant WA, Reichle M, Saucedo GJ, Tan S, Tayler G and Treiman J (2000) A Site-Conditions Map for Calofornia Based on Geology and Shear-Wave Velocity, Bull. Seism. Soc. Am., 90, 6B, S187-S208.

Zadeh LA (1965) Fuzzy sets. Information and Control, 8:338—353. 35.

Zimmermann HJ (2001) Fuzzy Set Theory and Its Application. Kluwer Academic Publishers. Boston/Dordecht/London. Fourth Edition.

# Footnotes

* Ilia Chavchavadze State University, Seismic Monitoring Center. Georgia.

e-mail: nato@seismo.ge; Tel: +995-32-210276; Fax: +995-32-210256.

** International Institute of Seismology and Earthquake Engineering , Building Research Institute. Japan.

e-mail: tyokoi@kenken.go.jp. Tel: +81-29-864-6756; Fax: +81-29-864-6777.

# Text boxes

Membership func.

Normalized Distribution Func.

0.1



x

0.

1.

Weights

High

0.9

Very Uncertain

Certain

0.7

Uncertain

0.5

Moderately Certain

0.3

Certain

0.1

b

a

Support

Core

R

Uncertain

Very Certain

Low

Uncertainty Level

U